## Slide 1: Key Idea 6: Aluminium (obtained from bauxite) is a strong, lightweight, rust resistant metal, used in items such as saucepans, bicycles, window frames and aeroplanes.
Understand and write equations for the purification of alumina from the bauxite ore (Bayer Process).
Describe and write equations for the redox process that occurs in the Hall-Heroult Cell.

## Slide 2: Aluminium: From Ore to Metal
Australia is the world’s largest producer of bauxite with substantial resources in WA, QLD and NT.
Aluminium is important for manufacturing as it is lightweight, strong, durable and can be recycled.

## Slide 3: Aluminium: From Ore to Metal
The steps for obtaining aluminium are:
Bauxite ore is mined
2. Bauxite is processed where it is treated to remove impurities
  – main impurities are iron oxide (Fe2O3) and
  silicon dioxide (SiO2)
  BAYER PROCESS
The result is white aluminium oxide or alumina (Al2O3)
Further processing by electrolysis in the
HALL-HEROULT CELL

## Slide 4
Bayer Process
Hall-Heroult Cell

## Slide 5: The Bayer Process
Bauxite is a naturally occurring material from which alumina (Al2O3) and aluminium metal are produced.
The principal minerals in bauxite are gibbsite (Al2O3.3H2O) boehmite (Al2O3.H2O)
Impurities in bauxite
    Clay
    Iron (III) oxide, Fe2O3
    Silicon dioxide, SiO2

## Slide 6: The Bayer Process
Step 1. The bauxite is washed and crushed, reducing the particle size and increasing the available surface area for mixture with hot, concentrated sodium hydroxide solution.
Alumina and silica react with hydroxide:
Alumina: Al2O3(s) + 2OH-(aq) → 2AlO2-(aq) + H2O(l)
Silica: SiO2(s) + 2OH-(aq) → SiO32-(aq) + H2O(l)

## Slide 7: The Bayer Process
Iron oxide (Fe2O3) does not react with hydroxide (because it is a basic oxide) and is filtered off to produce ‘red mud’

## Slide 8: The Bayer Process
Step 2: Water and seed crystals of alumina are added to the solution.
Hydrated alumina crystallises leaving the silicate ion in solution
2AlO2-(aq) + 4H2O(l) → Al2O3.3H2O(s) +2OH-(aq)

## Slide 9: The Bayer Process – Producing Alumina
  Step 3: The crystals are then separated off and dehydrated by roasting (heated).
  Al2O3.3H2O  Al2O3(s) + 3H2O(g)
  Alumina (Al2O3) is a white powder, which is the final product of the Bayer Process.
  This is then ready for shipment to aluminium smelters in the Hall-Heroult Process.

## Slide 10
The Bayer Process
Purification of alumina from bauxite ore

## Slide 11: Metal Reactivity Series - Aluminium

## Slide 12: Hall-Heroult Process is the Electrolytic reduction of aluminium oxide to aluminium
The commercial operation for reducing alumina to aluminium is an electrolytic process invented independently but simultaneously by Paul Heroult in France and Charles Hall in the US in 1886.
Huge quantities of electricity are required (10-13 kWh of electricity per 1 kg of aluminium) so aluminium smelters need to be located close to sources of cheap electric power.

## Slide 13: Molten electrolysis is used in the reduction of:
Potassium
Sodium
Calcium
Magnesium
Aluminium
Molten electrolysis is an expensive process as a considerable amount of energy is needed.

## Slide 14: Aluminium reduction- Molten Electrolysis
The reduction of aluminium ions to aluminium metal does not occur easily
Molten alumina is required for the last stage of aluminium extraction.
Alumina = Aluminium Oxide, Al2O3
Alumina has a very high melting point of approximately 2030°C

## Slide 15
Electrolysis of aluminium
https://www.youtube.com/watch?v=CglZBajYrME

## Slide 16
Carbon cathode lining
Steel lining
Al(l) tap
Molten mixture of alumina and cryolyte
Al(l) tap
Molten Al
Carbon anodes

## Slide 17: How it works
Anode
+
Cathode -
Al2O3
2Al3+ + 3O2-
Al3+
Al3+
Al3+
Al3+
O2-
O2-
O2-
O2-
O2-
O2-
Direct
Current

## Slide 18: At the anode
O2-
O2-
CO2
anode
O2
e- e-
e- e-
O2-
O2-
O2
e- e-
e- e-
2O2-

O2
+ 4e-
O2-
O2-
O2 + C  CO2
positive
+

## Slide 19: At the cathode
Cathode
e- e-
e-
Al
e- e-
e-
Al3+

Al
+ 3e-
Al3+
Al3+
Al
l
i
q
u
i
d
al
negative
-

## Slide 20: At the electrodes
At the negative cathode
Positive Aluminium ions drift to the cathode.
They gain electrons and become aluminium atoms
Al3+ + 3e-  Al
At the positive anode
Negative oxide ions drift to the positive anode.
They lose electrons and become oxygen gas molecules.
2O2-  O2 + 4e-
O2 + C  CO2
Liquid aluminium metal is
deposited at the cathode
Oxygen combines with carbon from the anode to produce carbon dioxide

## Slide 21: Reactions Summary Hall – Heroult Cell
ANODE reaction:
Oxide ions are oxidised to O2 and at the high temp. of the cell the carbon anodes are burnt and must be replaced periodically.
2O2-  O2(g) + 4e- AND
C(s) + O2(g)  CO2(g)
CATHODE reaction:
Aluminium ions are reduced to aluminium metal.
Al3+ + 3e-  Al(l)
OVERALL reaction:
4Al3+(l) + 6O2-  4Al(l) + 3O2(g) OR
4Al3+(l) + 6O2-(l) + 3C(s)  4Al(l) + 3CO2(g)

## Slide 22: Hall-Heroult Cell
The O2 produced at the anode reacts with the graphite.
C + O2 CO2

## Slide 23: Aluminium reduction- Molten Electrolysis
Temperature of reaction
  Alumina is dissolved in molten cryolite (Na3AlF6) which decreases its melting point from 2030°C to just under 1000°C and also increases conductivity of the solution.
  This is A LOT more economical but still requires a large amount of energy.
  Alumina electrolyte is added continuously to replace the alumina that is consumed by the reaction.

## Slide 24: Summary of Hall-Heroult cell
Cyrolite (Na3AlF6): “FLUX”
  Lowers the temperature at which Al2O3 melts from 2020oC to 900oC
  Saves electricity for heating and therefore money.
Cathode (reduction)
  At 900oC and above…
  Al2O3(s)  2Al3+(l) + 3O2-(l)
  Al3+(l) + 3e-  Al(l)
  Liquid aluminium forms and settles at the bottom of the Hall-Heroult Cell.
Anode (oxidation)
  2O2-(l)  O2(g) + 4e-
  Problem: the anode is made up of graphite/carbon and at 900C, the oxygen formed at the anode reacts with the anode.
    C(s) + O2(g)  CO2 (g)
  Therefore the anodes have to be periodically replaced.

## Slide 25: Final Stages of Hall-Heroult Process
Molten aluminium is more dense than cryolite and collects on the cell bottom where it forms the operating cathode. It is normal to operate a cell with a pool of aluminium 10 cm deep, the metal being siphoned off daily to maintain this level.
The metal is generally cast as ingots, which are at least 99 % pure with small amounts of iron and silicon being the main impurities.
Alternatively, the metal is kept molten in a furnace to which other elements are added to make alloys, prior to cooling.
Metal of up to 99.999 % purity is produced by further refining.

## Slide 26
Suggest 3 examples of uses for aluminium and which properties of the metal make it suitable.
Give 3 reasons why to recycle aluminium

## Slide 27: Uses of Aluminium
Aluminium is the most widely used metal after iron. Its properties include:
  low density,
  malleable and easily worked,
  corrosion resistant and
  good conductor of both heat and electricity.
With the exception of corrosion resistance, all these properties can be improved or augmented by alloying aluminium with small amounts of other metals.
It is therefore not surprising that aluminium has a very wide range of applications.

## Slide 28: Uses of Aluminium
1) Low density and strength make aluminium ideal for construction of aircraft, lightweight vehicles, and ladders. An alloy of aluminium called duralumin is often used instead of pure aluminium because of its improved properties.
2) Easy shaping and corrosion resistance make aluminium a good material for drink cans and roofing materials.
3) Corrosion resistance and low density leads to its use for greenhouses and window frames.
4) Good conduction of heat leads to its use for boilers, cookers and cookware.
5) Good conduction of electricity leads to its use for overhead power cables hung from pylons (low density gives it an advantage over copper).
6) High reflectivity makes aluminium ideal for mirrors, reflectors and heat resistant clothing for fire fighting.

## Slide 29: Why recycle aluminium?
Aluminium ores could run out
Extraction of aluminium uses lots of electricity and so is very costly
Production of the greenhouse gas carbon dioxide during the process
Loss of landscape due to mining, processing & transporting bauxite ore.
Loss of landscape for electrolysis plant
Noise pollution
Pollution involved in energy generation
Avoids need to dump old aluminium if it wasn’t recycled.

## Slide 30
Full process
https://www.youtube.com/watch?v=WaSwimvCGA8
Ant hill castings
https://www.youtube.com/watch?v=EWVx9K7KwBA

## Slide 31: Key Idea 7: Precipitation reactions are when an insoluble compound (solid) is formed from two solutions mixing. These are sometimes used in metal extractions.
Observe some precipitation reactions and write fully balanced equations for the reactions that occur.

## Slide 32: Precipitation reactions
Precipitation reactions occur when cations and anions in aqueous solution combine to form an insoluble ionic solid called a precipitate. Whether or not such a reaction occurs can be determined by using the solubility table for common ionic solids.

## Slide 33: Precipitation reactions
The solids produced in precipitate reactions are crystalline solids, and can be suspended throughout the liquid or fall to the bottom of the solution.
The remaining fluid is called supernatant liquid. The two components of the mixture (precipitate and supernate) can be separated by various methods, such as filtration, centrifuging, or decanting.

## Slide 34: Double displacement reactions
AB(aq)+ CD(aq)→ AD(aq)+ CB(s)
AB and CD are usually aqueous ionic compounds consisting of aqueous ions (A+ and B-, C+ and D-).
When a double displacement reaction occurs, the cations and anions switch partners, resulting in the formation of two new ionic compounds AD and CB, one of which is in the solid state. This solid product is an insoluble ionic compound called a precipitate. To determine whether a product ionic compound will be soluble or insoluble, consult a Solubility table .
If both of the predicted products are soluble, a precipitation reaction will not occur.
Example: 2NaOH(aq) + MgCl2(aq) →

## Slide 35: Double displacement reactions
AB(aq)+ CD(aq)→ AD(aq)+ CB(s)
Example:
2NaOH(aq) + MgCl2(aq) → 2NaCl(?) +Mg(OH)2(?)
To determine if a precipitate occurs, use the solubility table to predict the states of the products.

## Slide 36: 2NaOH(aq) + MgCl2(aq) → 2NaCl(?) + Mg(OH)2(?)

## Slide 37: Double displacement reactions
Answer:
2NaOH(aq) + MgCl2(aq) → 2NaCl(aq) +Mg(OH)2(s)
Now you try:
barium chloride + sodium carbonate → ?
BaCl2(aq) + Na2CO3(aq) →

## Slide 38: Double displacement reactions
BaCl2(aq) + Na2CO3(aq) → BaCO3(s) + 2NaCl(aq)
barium chloride sodium carbonate barium bicarbonate sodium chloride

## Slide 39: Precipitation of minerals
Precipitation, like crystallisation is the reverse of dissolving.
If a solid comes out of solution slowly, a regular, solid lattice has time to form and large crystals are produced.
                If the solid is formed quickly, there is no time for a large, solid lattice to grow and instead many particles form in the liquid (precipitation)

## Slide 40: Precipitation of minerals
Mineral precipitate. A mineral deposited from a water solution in pores or other openings in rocks. Chemical reaction with the surrounding rock, changes in pressure or temperature, or just drying up (evaporation) can cause a mineral to precipitate out of solution.
Quartz veins are common products
of mineral precipitation.

## Slide 41: Precipitation reactions practical
 | NaCl | Na2CO3 | Kl | NaOH
BaCl2 | - | + | - | -
AgNO3 | + | + | + | +
Pb(NO3)2 | + | + | + | +
CuSO4 | - | + | + | +
FeSO4 | - | + | + | +

## Slide 42
 | NaCl | Na2CO3 | Kl | NaOH | 
BaCl2 | - | BaCl2 + Na2CO3 → BaCO3+ 2NaCl | - | - | 
AgNO3 | AgNO3 + NaCl → AgCl + NaNO3 | AgNO3 + Na2CO3 → AgCO3 + Na2NO3 | AgNO3 + Kl → AgI + KNO3 | AgNO3 + NaOH → AgOH + NaNO3 | 
Pb(NO3)2 | Pb(NO3)2+ 2NaCl → PbCl2 + 2NaNO3 | Pb(NO3)2 + 2Na2CO3 → Pb(CO3)2 + 2Na2NO3 | Pb(NO3)2 +2Kl → PbI2 + 2KNO3 | Pb(NO3)2 + 2NaOH → Pb(OH)2 + 2NaNO3 | 
CuSO4 | - | CuSO4 + 2Na2CO3 → CuCO3 + Na2SO4 | CuSO4 + 2Kl → CuI2+K2SO4 | CuSO4 + 2NaOH → Cu(OH)2 + Na2SO4 | 
FeSO4 | - | FeSO4 + Na2CO3 → FeCO3 + Na2SO4 | FeSO4 + 2Kl → FeI2 + K2SO4 | FeSO4 + NaOH → Fe(OH)2 + Na2SO4 | 

## Slide 43: Precipitation Reactions
Silver nitrate + sodium chloride 
Silver nitrate + sodium bromide 
Silver nitrate + potassium iodide 
Lead nitrate + sodium chloride 
Lead nitrate + sodium bromide 

## Slide 44: Precipitation Reactions
6) Lead nitrate + potassium iodide 
7) Lead nitrate + sulfuric acid 
8) Barium chloride + sulfuric acid 
9) Copper sulfate + sodium carbonate 
10) Magnesium sulfate + sodium carbonate 